## Slide 1: TOD Down-Sampling
Jonah Lee

## Slide 2: Possible Methods
Sampling nth value (lose information)
Windowed average
  Naive average - this is what I have done at the moment
  Weighted values at borders (Chapin et. al sec. 3.1.1)
FFT truncation

## Slide 3: Image Differences (see speaker notes)
x1
(original)
x10
x50
x100
Notes: According to the rule of thumb described in Chapin et al. Section 3.1.1, we get:
beam size: 54" (from config)
scan speed: ~566"/s (from plot)
3 samples per beam
→ 30Hz minimum sample rate for BLAST-TNG
Data is natively sampled at 477Hz so this would correspond to a maximum downsampling factor of 15.9, which aligns with what we observe in the quality of the map.

## Slide 4: Performance Increase
Test was run for Roach 1 / Single pass.
Slice length before downsampling = 166700
Downsampling factor is equal to window width